## Slide 1: Biweekly Update Presentation 04
Berkay Ipek – ARPLab 13/08/2025

## Slide 2: Outline
What is done
  Linear Memory Analysis
  Memory Sweep Analysis
  Advanced Memory Sweep Analysis
Plans for the next weeks
  PRBS Signal

## Slide 3: What is done: Linear Memory Analysis

## Slide 4: Linear Memory Analysis: Set up

## Slide 5: Linear Memory Analysis – Set Up
Purpose: To check if non-linear memorial terms () are effective or not. If the system is working similar without non-linear memorial terms, then omit these terms.
Step 1: Take the signal of input and output @ 2 GHz
Step 2: Try to calibrate it with considering linear and non-linear terms. (for memory order 3 and polynomial order 3)
Step 3: Try to calibrate it with considering only linear terms.
Step 4: Compare the results and check magnitude of coefficients.
Step 5: Go to step 2, and do it other combination of orders.

## Slide 6: Linear Memory Analysis: Results

## Slide 7: Linear Memory Analysis – Results
Spectrum of output waveform in the buffer :

## Slide 8: Linear Memory Analysis – Results
Memory order 3 & Polynomial order 3 :
  Both linear and nonlinear: -38 dB | Only linear : -52.3 dB

## Slide 9: Linear Memory Analysis – Results
Memory order 3 & Polynomial order 3 :
  Both linear and nonlinear: -38 dB | Only linear : -52.3 dB

## Slide 10: So, is it working ??

## Slide 11: Linear Memory Analysis – Results
Memory order 5 & Polynomial order 5 :
  Both linear and nonlinear: -63.1 dB | Only linear : -48.5 dB

## Slide 12: Linear Memory Analysis – Results
Memory order 5 & Polynomial order 5 :
  Both linear and nonlinear: -63.1 dB | Only linear : -48.5 dB

## Slide 13: Linear Memory Analysis: Results Comparing

## Slide 14: Linear Memory Analysis – Results
Memory order 3 & Polynomial order 3 :
  Both linear and nonlinear: -38 dB | Only linear : -52.3 dB
Memory order 3 & Polynomial order 5 :
  Both linear and nonlinear: -56.8 dB | Only linear : -48.6 dB
Memory order 5 & Polynomial order 3 :
  Both linear and nonlinear: -38.5 dB | Only linear : -52.25 dB
Memory order 5 & Polynomial order 5 :
  Both linear and nonlinear: -63.1 dB | Only linear : -48.5 dB
Memory order 5 & Polynomial order 7 :
  Both linear and nonlinear: -82.8 dB | Only linear : -45.8 dB
Memory order 7 & Polynomial order 7 :
  Both linear and nonlinear: -88.2 dB | Only linear : -45.74 dB

## Slide 15: What is done: Memory Sweep Analysis

## Slide 16: Memory Sweep Analysis: Set up

## Slide 17: Memory Sweep Analysis – Set Up
Purpose: To check every possible cases to see which memorial coefficients can be omitted by doing a sweep.
Step 1: Take the signal of input and output @ 2 GHz
Step 2: Try to calibrate it with considering all terms. (@ fix memory order 5)
Step 3: Try to calibrate it with ignoring every possible memorial terms in the system (see next slides).
Step 4: Plot the results to detect which one has an interesting result.
Step 5: Go to step 2, and do it other combination of polynomial order.

## Slide 18: Memory Sweep Analysis – Set Up
Table for Memory Sweep

## Slide 19: Memory Sweep Analysis: Results

## Slide 20: Memory Sweep Analysis – Results
Polynomial order 5

## Slide 21: Memory Sweep Analysis – Results
Polynomial order 5 (Memory Sweep 0111)

## Slide 22: Memory Sweep Analysis – Results
Polynomial order 7

## Slide 23: Memory Sweep Analysis – Results
Polynomial order 9
Less # of coeffs

## Slide 24: What is done: Advanced Memory Sweep Analysis

## Slide 25: Advanced Memory Sweep Analysis– Set Up
Purpose: To check every possible cases to see which memorial coefficients can be omitted by doing a sweep.
Step 1: Take the signal of input and output @ 2 GHz
Step 2: Try to calibrate it with considering all terms. (@ fix memory order 7)
Step 3: Try to calibrate it with ignoring every possible memorial terms in the system (see next slides).
Step 4: Plot the results to detect which one has an interesting result.
Step 5: Go to step 2, and do it other combination of polynomial order.

## Slide 26: Memory Sweep Analysis – Set Up
Table for Memory Sweep
Do it for up to x(t-7)
Total of 128 cases, so only best 50 cases
will be plotted.
….
…. x(t-7)

## Slide 27: Memory Sweep Analysis – Results
Polynomial order 3

## Slide 28: Memory Sweep Analysis – Results
Polynomial order 5

## Slide 29: Memory Sweep Analysis – Results
Polynomial order 7

## Slide 30: Memory Sweep Analysis – Results
Polynomial order 9

## Slide 31: Plans for the next weeks

## Slide 32: Plans for the next weeks
Now, we decided which order is going to be used.
For the next week, implementation in digital domain will be analyzed and discussed.